## Slide 1: CS 231 – Chapter 2
Recall the 2 major components: CPU and RAM
  CPU contains registers for currently executing code
  Names: $s0-$s7, $t0-$t7, $f0-$f31, etc.
  A few registers have a special purpose.
RAM contains your program’s code + data
Similarly, an assembly program has 2 parts:
  Data segment: global variables, arrays, strings, real constants
  Text segment: instructions

## Slide 2: Data & I/O
“input, calculations, output”
A program performs calculations. On what data?
  Input taken during execution
  Small amounts of data encoded inside instructions
  Large amounts of data initialized before program starts
Output / outcome of program
  Always necessary 
  Could keep result temporarily in register or RAM
  Desirable at some point to perform output
  The OS handles file I/O analogously to standard I/O
  We will focus mainly on standard I/O.

## Slide 3: What to learn?
We are going to learn the MIPS assembly language.
Consider:
  What do we need to know when learning a programming language?
  What would we need to know how to do, in order to be decently proficient?
  If I could write a program that does _____, then I have mastered the essentials.
Take a moment to write a checklist of things you would hope to learn how to use a new language.

## Slide 4: Simple calculations
A HLL statement such as x = y + z; becomes an instruction that looks like add $s1, $s2, $s3
Register allocation
Destination register, source registers
Examples of routine instructions
  Assigning constant to register li $s0, 15
  Copying one register to another move $s3, $s4
  Arithmetic operations sub $s2, $s4, $s5
An assembly instruction can only perform 1 operation.
  What if we need more? x = (a + b) – (c + d);

## Slide 5: Complete program
Comment: Lines starting with #
Data segment
  .asciiz to declare strings
  .word to declare integers
  .space to set aside a certain number of bytes
  Other directives exist (.float, .double for reals)
Text segment
  Manipulate registers
  Use data segment as needed
  Special system call to end the program
Let’s look at 2 simple programs: hello.s and ex1.s

## Slide 6: More useful skills
Review I/O (iodemo.s) as needed
We’ll need 4 skills to use arrays in assembly:
  Declare in the data segment
  Access individual element
  Loop
  Compare numbers
So, we need to learn new instructions
  Conditional branch
  Unconditional jump
  Load and store

## Slide 7: Branch and jump
6 types, corresponding to relational operators in HLL
beq, bne, bgt, bge, blt, ble
Format example:
beq $s1, $s2, come_here
Meaning: “If s1 = s2, then go to the instruction beside the label called come_here:
You can use any word or phrase as your label. Make it meaningful. A compiler would just generate an arbitrary name like L73.
The jump instruction j is even easier. Go without asking questions! E.g. j come_here

## Slide 8: If versus loop
Surprisingly, both if-then statements and loops are implemented in assembly using the same collection of branch & jump instructions.
How can we tell when a branch or jump instruction is associated with a loop or not?
Examples:
  if.s (Consider: What if we need 2 comparisons?)
  1to10.s (Consider: How to change to count in reverse?)
When we count, use addi instead of add: we want to add a constant to a register

## Slide 9: Load & store
Registers are in the CPU. Arrays are not. We need load & store instructions to move back and forth.
Load: copy data from data segment to a register
Store: copy data from a register to the data segment
Examples:
lw $s1, 0($s2) | Load into $s1 a word from memory address $s2
lw $s1, 16($s2) | Load into $s1 a word from memory address ($s2 + 16)
sw $s1, 0($s2) | Store the $s1 value into memory at address $s2
sw $s1, 28($s2) | Store the $s1 value into memory at address ($s2 + 28)

## Slide 10: Notation
“Word” = 4 bytes
Load & store instructions take 2 operands
  First operand = register containing data
  Second operand = Address in memory for the data
Note that for store instruction, the destination operand appears last!
The memory address is stored in a register. We are allowed to add a constant to this register. Usually this constant is simply 0, e.g. lw $s1, 0($s2)
We also have instructions lb and sb for moving single bytes of data. This is useful for character/string data.

## Slide 11: Array addressing
We don’t use array index as in HLL.
Instead, we use address of array element we want.
Formula: total_addr = base_addr + offset
For an array of integers:
& a[ i ] = & a[ 0 ] + 4 * i
Sometimes, the offset is a constant. For example, a[6] is located 24 bytes from the beginning. If $s0 is the base address, we want 24($s0).
More likely, we use a loop, and a variable offset that changes on each iteration.

## Slide 12: Array example
Suppose we have an array of 100 integers.
A loop to traverse this array would need to do this:
For i = 0 to 99:
total_addr = base_addr + 4*i
Obtain the word @ total_addr
In practice, we may use separate registers for the base address, offset, total address, and the value of the array element.
Examples: array5.s, array.s, sumarray.s

## Slide 13: Review array & loop
Suppose a = array of 10 int, starting at address 700.
  The elements are at addresses 700, 704, 708, … 736.
  To traverse the array, some register needs to contain these addresses, one per iteration of a loop. We want to let s1 to range from 700 to 736, incrementing by 4.
Sumarray.s
  How many iterations?
  How many dynamic instructions?
Let’s write a loop that finds the sum 1-100.
  How many dynamic instructions?
  A little optimization
Ready for lab

## Slide 14: Addressing issues
How to calculate address in multi-dimensional array.
  Row major
  Column major
Numbering the bytes within a word
  Big endian
  Little endian
What if an array address calculation is incorrect?
  Could be accessing different variable
  Segmentation fault
  Bus error

## Slide 15: Multi-dimensional
Arrays with > 1 dimension are a HLL abstraction
RAM is just 1-D.
Given indices (row, col), need to compute offset.
2 strategies: row major & column major.
  Row major means rightmost index changes most frequently.
  In a HLL, the choice is made for you.
  If YOU are writing the assembly code, you get to choose.
0 | 1 | 2 | 3
4 | 5 | 6 | 7
8 | 9 | 10 | 11
12 | 13 | 14 | 15
0 | 4 | 8 | 12
1 | 5 | 9 | 13
2 | 6 | 10 | 14
3 | 7 | 11 | 15

## Slide 16: Byte order
Suppose the number 0x12345678 occupies a word of memory, at address 700.
What are the values stored in the individual bytes?
2 strategies: big endian and little endian. We ask, which byte of the number is stored at the first (i.e. lowest address) byte - most significant or least significant?
Choice is made by manufacturer.
Let’s look at bytes 700, 701, 702, 703 for big endian and little endian. Which one is which?
12 | 34 | 56 | 78
78 | 56 | 34 | 12

## Slide 17: Addressing errors
Minor logical error: Suppose $s0 is the base address of your array of integers. What does this instruction do?
lw $s1, -4($s0)
Segmentation fault
  Accessing an address outside of your program. It’s like going home to the wrong house.
  Common causes: address is 0, uninitialized, or you forgot to add base address
Bus error
  Unaligned address. Word address must be multiple of 4. It’s like selecting unmatching shoes.
Hackers intentionally address out of bounds to enter or corrupt your system!

## Slide 18: Functions
We use instructions jal and jr
Why not use instruction j to call function?
Convention (recommendation):
  Pass arguments in registers $a0-$a3
  Return values in registers $v0-$v1
When you enter a non-leaf function, save return address!
  e.g. main calls function a; a calls function b
Run-time stack
  $sp maintains address of next available place to “push”
  Grows in the negative direction
  Can be used to store additional parameters
  Can be used to preserve registers that the function needs

## Slide 19: Run-time stack
Can be used to store:
  $ra in case we call another function
  Arguments, if there are more than 4
  Any “s” registers we plan to use.
Convention:
  “t” registers are understood to always be available to you. “t” is for temporary.
  If you use a “t” register and then call a function, assume that the value will be lost when the function returns back to you.
  Your “s” registers should be saved at the beginning of the function, and then restored at the end. So, inside any function you have access to all “s” and “t” registers.

## Slide 20: Binary code
Everything in memory is in binary … even your code
Assembly language is just a different alphabet of the machine language. (Happens in human languages too)
The assembler:
  Checks syntax
  Resolves pseudo-instructions into true hardware instructions
  Calculates address of labels
  Generates binary code, 32 bits per instruction

## Slide 21: Binary code
Let’s practice encodings of: add, addi, lw
Notice there is no li
Branches
  Relative branch address calculation
  slt instruction
Jump
What else “doesn’t exist” in true assembly?
  e.g. mul, div, la
Can practice various instructions with MARS display to check our answers. Encode & decode.

## Slide 22: Integer
What is the 6-bit representation of –14 in:
  Unsigned
  Sign magnitude
  1’s complement
  2’s complement
  Biased 31
100011 is the 6-bit representation of which integer in those schemes?

## Slide 23: Extensions
“Extending” a representation means to allow a number to occupy more bits. e.g. 16  32 bits
Usually, we use the term “sign extension”
Unsigned
  Pad the left end of the number with 0’s
Sign-magnitude
  Move the sign bit to the far left end
  Pad with 0’s
1’s and 2’s complement
  Pad with sign bits

## Slide 24: Integer addition
Binary (2’s comp) examples can help us fill out a truth table. Notation: We add X+Y, put result in Z. C is the carry, and “i” is the index for the bit position, starting at 0.
What values go in the last 2 columns?
C(i) | X(i) | Y(i) | Z(i) | C(i+1)
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 25: Implementation
Look at truth table results. Consider:
  When is Z(i) = 1? When is C(i+1) = 1?
At first glance, we could say
  Z(i) = (C(i) + X(i) + Y(i)) mod 2
  C(i+1) = (C(i) + X(i) + Y(i)) div 2
We ought to use bitwise operations:
  Z(i) = C(i) xor X(i) xor Y(i)
  C(i+1) = (C(i) and X(i)) or (C(i) and Y(i)) or (X(i) and Y(i))
In HW, not implemented as code but as logic gates.

## Slide 26: Other topics
Subtraction: addition of the opposite
Overflow: Correct answer lies beyond the range of possible representable values
Symptoms:
  Sum of 2 positives = negative
  Sum of 2 negatives = positive
  Answer is surprisingly small in magnitude
Common misconception: Carry out of the leftmost bit always indicates overflow
Based on signs of operands, can tell if overflow possible or not

## Slide 27: Int multiplication
What is 99x99 ? Notice the number of digits.
In binary, (n bits) * (n bits) = prepare for 2n bit answer
HI & LO registers
2’s complement mult: Sign extend operands first
Example: (4 bit) * (4 bit): Try –3 * 6.
Multiplication is expensive. Opportunity to improve.
  11 cycles on the MIPS, 19 cycles on SPARC
  But add, sub, sll take just 1 cycle each.
Booth’s algorithm 
  e.g. 27 = 24 + 23 + 21 + 20 = (25 – 23) + (22 – 20)

## Slide 28: Real representation
One language: IEEE Floating Point Standard
Two sizes: 32 and 64 bits (single & double precision)
Let’s focus on single precision. Double is analogous.
Binary scientific notation, e.g. 1.11011 * 22
1 sign bit, 8 exponent bits, 23 mantissa bits
  Exponent in biased 127
  Mantissa includes a hidden bit, usually understood to be 1
  Mantissa is effectively 25-bit sign-magnitude
  If not exact, the mantissa may round due to finite length.
Practice both ways. e.g. what number is 0xc2250000?

## Slide 29: Special cases
Exponent “11111111” means infinity or NaN
Exponent “00000000” means denormalized number
  Either the number is 0, or it’s so small that we need to make the hidden bit 0.
Underflow
Graceful underflow
Other than special cases, range of exponents is –126 (00000001) to +127 (11111110).

## Slide 30: Investigate
How many significant figures do we have?
  Single precision bit allocation: 1 + 8 + 23
  Double precision bit allocation: 1 + 11 + 52
  Good design?
How would you double a number?
In single precision, what is the …
  Largest finite number?
  Smallest positive number?
  Smallest positive integer we cannot represent?
How many representations exist between two integers?

## Slide 31: MIPS f.p. instructions
Arithmetic
  add.s, add.d
  “.s” and “.d” versions of sub, mul, div, abs, neg
Converting (among integer “w”, single “s”, double “d”)
  cvt.d.s means to convert from single to double
  5 others
Moving
  mov.s, mov.d
  l.s, l.d, s.s, s.d
Comparing
  c.le.s, c.le.d
  c.lt.s, c.lt.d
  Followed by bc1t or bc1f